## Slide 1: Signed Integers, Extension, Truncation, and Addition
CS 0447
Jarrett Billingsley

## Slide 2: Class announcements
last day to add the class is this Friday 1/19 (but the waitlists are so long)

## Slide 3: Signed Integers

## Slide 4: The basic idea
if we want to have negatives, we need to come up with rules which…
  treat some bit patterns as negative values
  allow us to do arithmetic correctly
    like “a number and its negative should add up to 0”
where's the sign written in math?
how many signs are there?
+45
-19
0101
1000
how could we represent a sign in binary?
the sign bit is always the MSB – NOT "the first 1 bit"
+
-
for these slides I'm using 4-bit numbers to save space, but you always have to know how many bits the number is to know which is the MSB
Notes: - we write the sign in front…there are only two signs…
- so we could represent the sign with one bit, and use the MSB as that sign bit
- you have to know how many bits the number is before knowing where the sign bit is.
- this is why I've been writing leading 0s.

## Slide 5: Sign-magnitude? (this is not used for integers omg)
this leads us to an intuitive but suboptimal representation:
the bits after the sign bit are the distance from 0 (aka magnitude)
0
0000
0001
+1
0010
+2
0011
+3
1001
-1
1010
-2
1011
-3
1000
0100
+4
0101
+5
0110
+6
0111
+7
1100
-4
1101
-5
1110
-6
1111
-7
but what about 1000?
what is its distance from 0?
big problem: we have TWO ZEROES! +0 and -0
sign-magnitude is still used for floats. but not for integers.
arithmetic on S-M is also kinda difficult.
negating is easy in S-M: just flip the sign bit.
Notes: - having two zeroes is… a huge pain in the ass (and that's an understatement)
zero is a super common number and having to special-case for it everywhere is not great.
the arithmetic is more difficult because you have to have special cases depending on the signs of the inputs (add in some cases, subtract in others, adjust the sign of the output appropriately). a computer has to be built to apply those rules in the right cases, and it’s just a lot of extra work.

## Slide 6: Two's complement
1001 0110
for signed integers, we use two's complement. here's the idea:
MSB (sign)
-128s
64s 32s 16s 8s 4s 2s 1s
you can think of the MSB as having a negative value.
so what number does this represent?
when we say "signed integer", we mean 2's complement.
it is the only signed integer representation in widespread use today.
Notes: - thanks to previous student Stevie Priller for sharing this insight
- it's -128 + 16 + 4 + 2 = -106
- in the Long Long Ago, both s-m and 1's complement were used for ints… but 2's compl won. cause it's best.

## Slide 7: A weird number line
1110
-2
1101
-3
1100
-4
1011
-5
1010
-6
1001
-7
let's see the bit patterns for negatives in 2's complement.
0
0000
0001
+1
0010
+2
0011
+3
1111
-1
0100
+4
0101
+5
0110
+6
0111
+7
but wait, what about 1000?
1000
-8
now we only have one zero, and it's all 0 bits (whew)
but the tradeoff is that the number line is lopsided. we have one more negative than positives.
also how are we even getting the negative numbers from the positive numbers??

## Slide 8: A negative number with no positive counterpart
in 2's complement, to negate, you flip all the bits (0s become 1s and 1s become 0s), then add one.
  (the number you get from this is also called “the two’s complement” of the original number.)
  let's negate +1 (0001) to see, then negate that to get back.
but what do we get if we negate -8 (1000)?
1000
0111
+0001
0
you just add the sign bit like a normal place.
we negated -8 and got -8. that’s… weird.
FLIP
1
1
1
0
0
1
Notes: - flip(0001) = 1110; then add 1 to get 1111. that's -1.
- to get back, flip(1111) is 0000; then add 1 to get 0001. that's +1 again.
- Honestly, I wish we settled on using this "most-negative-integer" as an "invalid value", like a "null for ints"
- but we didn’t. and now we always have this weirdo value. wahhhh

## Slide 9: The signed number tradeoff
if you have signed numbers, why would you want unsigned ones?
well, let’s look at the number lines for 4-bit unsigned and signed ints.
0
15
+7
-8
0
7
8
...
...
there is the same number of numbers on both (24 = 16).
signed numbers present a tradeoff. you get to represent negative numbers… at the expense of losing half the range on the positive side of the number line!
Notes: it’s like we cut the unsigned number line between 7 and 8, then moved that upper part to the left of 0 and reassigned the meanings of those bit patterns. what was 8 (1000) becomes -8, what was 9 (1001) becomes -7, etc.
  but we didn’t get any new bit patterns. we’re still stuck with 4 bits.
as a side note, the overlapping portion of the two number lines (here, 0 to 7) is the “safe” range of numbers that can be represented as both signed and unsigned integers. so in languages with both, only numbers in that range will preserve value when converted between signed and unsigned “flavors” of ints.

## Slide 10: Range of unsigned vs. signed numbers
how many different values can you represent with n bits?
  2n
and what are the smallest and the biggest?
  0 to 2n-1… for unsigned integers.
well, for signed numbers, the range is -2n-1 to 2n-1-1
that feels kinda awkward, so let's get some intuition…
in 2’s complement, half of the bit patterns are assigned negative values.
so if you know the unsigned range, chop it in half.
8 bits unsigned = 0 to 255, so…
8 bits signed is -128 to +127.
0
15
+7
-8
0
7
8
...
...
Notes: and remember, there's always one more negative number than positive.

## Slide 11: Extension and Truncation

## Slide 12: Changing the number of bits
integers on computers have a fixed number of bits.
but what happens in this situation?
    byte b = 10; // 8 bits
    int i = b; // 32 bits
you would (reasonably) expect that i == 10, and sure enough it does.
  but how does that happen? how did we go from 8 bits to 32?
also what happens in the other direction?
    int i = 20;
    byte b = i; // error: “possible lossy conversion”
the compiler complains about this, so we have to write…
    byte b = (byte)i; // ok!
why?

## Slide 13: Zero extension
let’s start with unsigned numbers. you can always put 0s before a number – so-called “leading 0s” – without changing its value.
10012
= 910
if I now put a 0 in front…
010012
= 910
that doesn’t change the value. all I said is “there are 0 16s.”
in fact, I can add as many 0s to the front as I want!
10012
= 010012
= 0010012
= 00010012
= 000010012
etc…
= 910
this is called zero-extension. it allows you to expand unsigned numbers to larger numbers of bits without changing their value.

## Slide 14: But that doesn’t work for signed numbers.
signed numbers are a bit trickier, because the MSB is special.
01112
= +710
if I now put a 0 in front…
001112
= +710
that seemed to work, but notice how the sign bit moved?
what happens if I try to do it to a negative number?
10012
= -710
if I now put a 0 in front…
010012
= +910
uhhhhh what
zero extension does not work for signed integers.
Notes: or if you want to be pedantic, zero extension works only on positive signed integers and fails on negative ones.
but an operation that only works “some of the time” isn’t very useful, is it?

## Slide 15: Sign extension (animated)
because the MSB of signed integers has a special meaning, we have to do different things depending on whether it’s a 1 or a 0.
sign extension puts copies of the sign bit before the number.
10012 (-710)  to 5 bits  110012 (-710)
01112 (+710)  to 5 bits  001112 (+710)
I like to think of it like spreading peanut butter…
1011
111111111111
why does this work? consider 10012. the MSB is -8. if I put a 1 before it, the MSB is now -16, and the next lower place is 8. -16+8 = -8, the same as what we started with, so the value remains unchanged.
Notes: sign extension is important because it preserves the sign and value of signed numbers!
if you think of the original MSB as having a value of “-m”, then because each place is 2 times the next lower place, adding a 1 in front of a negative number is like adding “-2m + m”, which is “-m”, which is what you started with. this generalizes to any number of 1s you put in front (e.g. adding 11 in front is like adding “-4m + 2m + m” which is “-m”).

## Slide 16: Truncation
”truncate” means to cut short, and for our purposes it means “cutting off bits on the left side of a number.”
000010012
= 910
if I truncate this unsigned integer to 4 bits, I get…
10012
= 910
the value was preserved, cause I just cut off leading 0s.
but if I keep going, strange things happen.
0012
= 110
I cut off a 1, and now I ended up with a different value!
this is what the Java compiler means about “possible lossy conversion”: sometimes, losing bits can change the value!
10012
= -710
0012
= +110
for signed integers, you can get even weirder results.
Notes: truncation doesn’t always give you a different value. the first example worked fine.
  the rule is, “if the value fits into the range of representable values for the target number of bits, it will work, otherwise you will get strange results.”
  in the first example, 9 is in the range of representable values for 4 bits (0 to 15), so it works.
  but in the second example, 9 is not in the range of representable values for 3 bits (0 to 7), so it fails.

## Slide 17: Truncation and modular arithmetic
let’s see what happens if we truncate 4-bit unsigned ints to 2 bits.
Original | Truncated
00002 = 010 | 002 = 010
00012 = 110 | 012 = 110
00102 = 210 | 102 = 210
00112 = 310 | 112 = 310
01002 = 410 | 002 = 010
01012 = 510 | 012 = 110
01102 = 610 | 102 = 210
01112 = 710 | 112 = 310
10002 = 810 | 002 = 010
10012 = 910 | 012 = 110
the value you get after truncation to n bits is not arbitrary. it is the original number modulo 2n!
here, n = 2, so the truncated values are the original numbers modulo 22 = 4.
remember when we tried to do unsigned 11112 + 00012? what happens if we truncate the result to 4 bits?
Notes: remember modulo gives you the remainder after dividing. so when I say “modulo 2n”, that means “the remainder after you divide by 2n.”
11112 + 00012 = 100002, but truncated to 4 bits, it’s 00002, because it’s modulo 24 = 16!

## Slide 18: Integers aren’t on a line, they’re on a circle!
because of this behavior, integers wrap around, like on a clock.
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
unsigned integers:
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
signed integers:
the same positions are represented by the same bit patterns…
but the meanings are different.
adding goes clockwise; subtracting goes counterclockwise.
what is -2 + 5?
what is 14 + 5?
Notes: - there’s an interactive version of this on my page! Materials, Reference, The Number Circle.
- -2 + 5 takes us to 3, which is correct… interesting
- 14 + 5 takes us to 3, which is weird, but makes sense in this number circle
- this is modular arithmetic: we say 14 + 5 = 3 mod 16.
- negation mirrors across the vertical axis
- so 0 is its own mirror, and so is the most-negative-integer!

## Slide 19: Addition and subtraction

## Slide 20: Two's complement addition
1101
3
+-6
-3
the whole reason two’s complement is so useful is that addition is dead simple. you can add any pair of two’s complement numbers using the same procedure as we learned for unsigned numbers.
3
+10
13
1
+1010
0011
1101
1
+1010
0011
to binary?
bit pattern for -6 is… -8+2
8 + 4 + 1 is…
the actual patterns of bits are the same. so how does a computer "know" whether it's
doing signed or unsigned addition?
-8 + 4 + 1 is…
Signed
Unsigned
it Just Works™.

## Slide 21
IT DOESN'T

## Slide 22: It's up to you!
the computer only knows one way to add numbers together.
the meaning or interpretation of the inputs and output of the addition are decided by you, the programmer.
in languages where you have signed and unsigned integers (e.g. C), you make this decision by choosing the type of the variable:
      int x = -5;
      unsigned int y = 20;
  when these variables are printed, added, subtracted etc. they will be interpreted as signed or unsigned accordingly.

## Slide 23: Subtraction
is subtraction really that different from addition?
  x - y == x + -y
  and in two's complement, -y == flip(y) + 1, so…
x - y == x + (flip(y) + 1)
7
-4
3
0111
+1100
1
there’s a carry out from the MSB, but because the result is truncated back to 4 bits, it’s thrown out.
7
+12
3
=
this is typically how computers do it, since we can reuse the same circuit for both addition and subtraction.
1
1
1
0
0
assuming 4-bit numbers…
Notes: 410 = 01002, and when we flip that we get 10112 = 1110, then + 1 = 1210.
well... the carry out from the MSB isn’t ALWAYS thrown out. later in the course we’ll learn more about what it indicates.

## Slide 24: What is two’s complement doing, anyway?
on the previous slide, we saw that in 4-bit arithmetic:
  the two’s complement of 4 is 12, and
  adding 12 behaves the same way as subtracting 4.
why? it all comes back to the number circle.
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
if we start at 7, we can subtract 4 by going counterclockwise…
…but because it’s a circle, there are two ways around it. we can also go clockwise by 12, which is the two’s complement of 4!
a number’s two’s complement behaves like its negative under modular arithmetic.

## Slide 25: Comparison with subtraction
subtraction is also how we compare numbers.
if we do a - b, for any a and b…
a > b
If…
then a - b will be…
positive (>0)
a < b
negative (<0)
a == b
zero
how can you quickly see if an integer is negative?
also, does this remind you of a certain Java method for comparing things…?
Notes: you look at the sign bit (MSB)!
the Comparable.compareTo() method uses this convention for the return value. a.compareTo(b) is positive if a > b, negative if a < b, and 0 if a == b. (in C, strcmp() also uses this convention.)