## Slide 1: CPU Intro
CS 0447
Jarrett Billingsley

## Slide 2: Class announcements
hoping to have exams graded by end of next week (10/18)
completely unrelatedly, monitored withdrawals are due by 10/25
  that’s also when final exam conflict requests are due
when project???? soon
also lectures for the next few weeks may run under/over, topics are being shuffled around

## Slide 3: ISA and hardware design

## Slide 4: Remember what an ISA is?
it's the software interface the programmer uses to control the CPU
what are some important aspects of the MIPS ISA?
how many registers does it have?
how big are they?
what instructions does it have?
how does it access memory?
how are they encoded into binary?
are there any special registers?
how many operands do they have?
the ISA abstracts the hardware design
but the hardware must implement the ISA, so…
Notes: - Instruction Set Architecture
- it has 32 32-bit registers, plus 3 more…
- $zero is always 0, and ra is used by jal, but otherwise they're identical
- HI and LO are 32 bits and are used by the multiplication and division instructions
- the PC is 32 bits and is its own thing
- it has lots of instructions: arithmetic, conditional branches, loads and stores, jumps…
- instructions can have 0-3 operands, of which 1 or 2 can be sources, and 0 or 1 can be destinations
- there are actually 3 instruction formats: R, I, and J
- only loads and stores access memory
- it can access 8, 16, or 32-bit values from memory
- the memory address that is accessed is a register + an immediate offset

## Slide 5: Tension you can cut with a knife
designing an ISA is an act of balancing many, many factors.
more registers!
more powerful instructions!
more bits!
run this popular language fast!
make the OS faster!
propagation delay!
materials cost!
power and heat!
manufacturing ability!
verifiability!
the users have demands…
…and the implementers have limits.
Notes: - verifiability means "mathematically proving that your design is right and has no bugs," which is often left in the dust in favor of constantly churning out new features and performance improvements
- which is how we've gotten where we are now, with hundreds of bugs and dozens of vulnerabilities in our CPUs
- yes, hardware can absolutely have bugs too. doesn’t that make you feel all warm and fuzzy?

## Slide 6: Meeting in the middle
first we broke software into small pieces
now we'll build hardware from small pieces
????????????????
MUXes, FSMs, etc.
Gates and Latches
Transistors
Physics and Electricity
Control Structures
ASM Instructions
Machine Code
the ISA specifies the software interface to the CPU…
but what does the CPU look like? what parts does it have? how does it understand the instructions?
where does the magic happen?
Notes: - in most complex systems, the "magic" comes from the ways things are interconnected, rather than from the pieces themselves
- this is what the overused phrase "more than the sum of its parts" means

## Slide 7: Microarchitecture
microarchitecture is the hardware design of a physical CPU.
a microarchitecture is an implementation of an ISA.
and like interfaces in Java, there can be many implementations of the same ISA.
interface X86_64
class Core_i7 implements X86_64
class Zen implements X86_64
class Nano implements X86_64
but there is a lot of freedom in how the CPU actually implements that interface.
Notes: - we may have been using x64 for almost 20 years, but the CPUs today are drastically different in design than the original x64 designs.
- abstraction gives us a lot of freedom to change things!

## Slide 8: Only kinda sorta MIPS
we'll use MIPS for context…
  but this stuff applies to virtually any architecture.
  such as the architecture you'll implement for the last project!!
the book doesn't use "real" MIPS either
  it uses DLX: a simplified, modernized version of MIPS
  the hardware in the book is extremely hand-wave-y (what's jal?)
  but they go into way more detail than needed for some things…
Notes: - the section on the ALU is, like, woah guys, we get it. you designed a CPU.

## Slide 9: CPU Organization

## Slide 10: Remember this?
Control
Registers
ALU
Processor
Memory
unresolved questions:
what's the control?
what's the ALU?
how does it know what instruction to get next?
how does it know which registers to access?
how does it know whether it should add, subtract, etc.?
Program
instruction
3
5
+
8
A
B
C

## Slide 11: Zooming in
there are a few major parts of any CPU:
Control
Registers
ALU
t0
s4
at
fp
eax?
sp
+
-
×
÷
⊕
∫
&
hi i'm memory!!
registers hold the values being computed
the ALU computes new values
☃
if(add)
do this
else if...
values move between them
the control tells everything else what to do, and when
control signals!
Notes: - what, you've never seen the snowman operator?

## Slide 12: OKAY, MEMORY, WHAT DO YOU WANT??
registers are just a temporary stopping point for your program's data
you could have a computer with few/no registers at all!
Control
ALU
Memory
this is a memory-memory machine
if you squint and wave your hands really hard, every computer is.
the registers and the memory only differ in their speed and size.
Notes: - really, we only have registers because our memory technologies are imperfect and we have to play to the strengths of each.
- if we suddenly had a breakthrough in memory technology, we could unify the registers, memory, and persistent storage and be done with it.

## Slide 13: Parts of the CPU

## Slide 14: Architectural and general-purpose registers
Microarchitectural
Architectural
the registers that the ISA specifies are the architectural registers
and of those, the general-purpose registers (GPRs) are the ones that you can use for any purpose in your programs
GPRs
tx
ax
vx
sx
sp
fp
zero
kx
pc
hi
lo
microarchitectural registers exist outside the ISA and are instead part of the implementation of the CPU.
they're used for temporary storage, to implement multi-step operations, to control special features, etc.
they are often (but not always!) inaccessible from software.
Notes: - many CPUs have debugging registers that are not accessible by normal means, but can be accessed through "secret" means like JTAG (a way of debugging hardware)
- there are often "temporary" registers the CPU uses to implement multi-step (complex) instructions

## Slide 15: The register file
the register file holds the general-purpose registers.
it's like an array of registers, or a small word-addressed memory.
notice how the MIPS registers are numbered?
D
Q
en
D
Q
en
D
Q
en
D
Q
en
etc…
D
Q
en
D
Q
en
$0
$1
$2
$3
$4
$5
register number go in…
register value come out.
maybe two at a time.
that might be useful.
and we should also be able to put values into them, too.
don't worry, we'll see how it works. but that's really all it is.
Notes: - dunno why it's called a file... it's likely historical.
- actually we don't need a register for $0, since it's just….. zero……………….

## Slide 16: The Arithmetic and Logic Unit (ALU)
the ALU takes old values and produces new values from them.
ALU
in all the arithmetic and logic (bitwise) instructions, how many input operands are there?
what kind of operations do we have to be able to do?
A
B
+
-
×*
÷*
&
|
~
<<
>>
>>>
*multiplication and division are kinda weirdos…
Notes: - 2. allllways 2.
- we might consider putting mult/div in their own unit, separate from the ALU, but right next to it.
- cause they're slower.
- we'll talk about this okay

## Slide 17: The program counter and control
Control
the PC register is part of the control: it says what step to do next.
Memory
0xAC30
PC
the PC is a memory address, so we send that to memory.
the memory sends back some data: an instruction.
0xC0DE
the control decodes the instruction and tells everything else what to do.
this is an add instruction!
the source regs are t0 and t8…
Notes: - ooh, maybe that instruction goes into a microarchitectural register!

## Slide 18: The bottomless pit of control
the registers and ALU are actually pretty simple.
control is where things get… interesting.
  we'll be studying the simplest kinds of control
  but there's no real upper limit on the complexity of control.
  in a sense, CPU design is control design. the other parts are largely interchangeable.
Notes: - and when I say interchangeable, I mean it – it's common for CPU designers to reuse parts of CPUs in many designs, even in implementations of different ISAs!
- e.g. AMD made a RISC ISA, the 29k, which didn't last for long…
- but their K5 (Pentium equivalent) was a 29k with an x86 instruction decoder bolted on the front and it worked pretty damn well
- funny cause that's basically how all x86 CPUs are now designed

## Slide 19: What the CPU does
all the parts of the CPU work together to do the CPU’s job: to read and execute instructions. it does this for every instruction:
Control
Registers
ALU
Processor
Memory
it fetches the next instruction to execute from memory;
then the control decodes (reads) the instruction;
then the control executes the instruction by telling the other parts what to do.
fetch, decode, execute. once per instruction.
Program
instruction
👀
read registers t2 and t4! add their contents! put the result in register a0!

## Slide 20: If every instruction has to be fetched from memory…
…then how many times is memory accessed for a load or store?
lw t0, var
Memory
123
...
var
for a load, we do one access to fetch the instruction…
Control
Registers
ALU
…and a second access to actually load the value!
a store would store the value on the second access.
this is going to have Implications™️ for how we implement loads and stores later…