## Slide 1: Addition and Overflow
CS 0447
Jarrett Billingsley

## Slide 2: Class announcements
yay it’s fall!

## Slide 3: Binary addition, in logic

## Slide 4: Solving problems with circuits
here's a surprising fact:
  all computation can be built from just the basic Boolean logic operations (AND, OR, and NOT).
  and since binary only has two values, anything expressed in binary can be computed using these logical operations.
our goal is to build an entire CPU.
  we'll hold off on the "reading instructions" and "taking steps" and "remembering stuff" until later.
  but we actually know enough already to start building the ALU: the part of the CPU that, well, computes.

## Slide 5: Quick aside: truth tables with “multiple outputs”
we’ll be looking at several truth tables that look like this:
A | B | X | Y
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | 1 | 0
A | B | X
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
A | B | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
here A and B are inputs, and X and Y are outputs. if that looks weird, well:
it’s shorthand for two truth tables. we’re just saving space by not repeating the inputs.
=
Notes: - remember, functions can only have one output! often we want to have “multiple-bit outputs”, but we do that be implementing each bit of the output as its own function.

## Slide 6: Is a half-truth a lie?
let's come up with a truth table for adding two 1-bit numbers.
each column will hold 1 bit.
A
B
C
0
0
1
1
0
1
0
1
0
0
0
1
S
0
1
1
0
let's name the inputs A and B:
and let's name the outputs C and S, for Carry and Sum.
for the input values, we count up in binary…
now let's fill in the output values.
great! But this is wrong.
hey, this C column looks familiar… what about S?
Notes: - whenever making a truth table, ALWAYS count up in binary – it's so easy to miss cases if you jump around
- C and S form a 2-bit number
- C just looks like A & B
S looks like A xor B
well it’s not wrong, it’s just not the whole answer, because we almost always need to add more than two 1-bit numbers together!

## Slide 7: The full truth
what we just made was a half-adder.
it has a carry output but not a carry input.
  (which might be useful for the lowest bit)
    but might not be, as we'll see
to make a full adder, we need 3 input bits:
A
B
Co
0
0
1
1
0
1
0
1
0
0
0
1
S
0
1
1
0
0
0
1
1
0
1
0
1
Ci
0
0
0
0
1
1
1
1
0
1
1
0
1
0
1
1
00111 110
1011 0010
+0010 1111
1110 0001
A
B
Co
S
Ci
Notes: - Ci = Carry in, Co = Carry out

## Slide 8: The logic of it all
it looks a little messy, but it kinda makes sense if you think of it like this:
  it counts how many input bits are "1".
if we look at the outputs in isolation:
  S is 1 if we have an odd number of "1s"
  Co is 1 if we have 2 or 3 "1s”
actually coming up with collections of gates that output this truth table is kind of complicated, but I’m just gonna wave my hands and say…
  there's a full_adder.circ example circuit for you!
A
B
Co
0
0
1
1
0
1
0
1
0
0
0
1
S
0
1
1
0
0
0
1
1
0
1
0
1
Ci
0
0
0
0
1
1
1
1
0
1
1
0
1
0
1
1
Notes: - Again, Co and S are a 2-bit number
- it might not be obvious, but we can come up with a collection of gates that output each of these columns

## Slide 9: Sweeping that under the rug…
in programming, we use functions to be able to reuse code.
in schematics, we can group these 5 gates into a component.
here's the symbol for a one-bit full adder:
+
B
A
Ci
Co
S
inputs are like parameters…
and outputs are like return values.
now we don't have to care how it adds, just that it does.
unfortunately Logisim’s built-in adder flips this upside down but whatever.
Notes: - Logisim does this with a lot of components (puts the least significant bit up top instead of at the bottom) and I don't know why. most diagrams I've seen in texts put the LSB at the bottom.

## Slide 10: And that’s how we build circuits
the process of building any circuit goes something like this:
A | B | Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
1. make a truth table that expresses the computation we want.
2. turn the truth table into a Boolean expression.
3. turn that into logic gates.
A
B
Y
steps 1 and 3 are pretty obvious, but step 2…
well, lab 5 will introduce you to a straightforward way to do that!
Notes: bubbles on the inputs of a gate are shorthand for a NOT gate on each bubbled input.
“turning a truth table into a boolean expression” can actually be a pretty complicated process! look up “karnaugh maps!”

## Slide 11: Adding (and subtracting) multi-bit numbers

## Slide 12: Where do the carries go?
when you add one place, you might get a carry out.
that bit becomes the carry in for the next higher place.
1 0 1 1 0 0 1 0
+0 0 1 0 1 1 1 1
Bit Bucket..?
Notes: - what is this called?
- how can we handle it?

## Slide 13: Ripple Carry
if we want to add two three-bit numbers, we'll need three one-bit adders!
we chain the carries from each place to the next higher place, like we do on paper.
we split the numbers up like so:
+
B0
A0
S0
+
B1
A1
S1
+
B2
A2
S2
A2 | A1 | A0
B2 | B1 | B0
S2 | S1 | S0
+
Logisim’s built-in multi-bit adders do this stuff for you.
Notes: - it's called ripple carry because the carry "ripples" from the LSB to the MSB one place at a time
- well, okay, Logisim's multi-bit adders are just using the + operator because they're written in Java but CONCEPTUALLY, OKAY?

## Slide 14: Propagation Delay
electrical signals can't move infinitely fast, and transistors can't turn on and off infinitely fast.
every gate and wire has propagation delay: the amount of time needed for a signal to “propagate” through it.
in a ripple carry adder, since each place must wait for the next smaller place to compute its “final answer” for its carry output…
  ripple carry is linear in the number of bits!
that means if you double the number of bits, you double the amount of time needed.
there are more efficient ways of adding…
  details, schmetails
+
B0
A0
S0
+
B1
A1
S1
+
B2
A2
S2
Notes: - carry lookahead adders are faster (constant time, O(1)!) but require O(n^2) space. there are several other kinds of adders too.
- I think there are also some diminishing returns there, so what you usually see is a weird hybrid approach:
- they do look-ahead carry on chunks of bits (fractions of the word size), and then ripple those carries to the next chunk of bits
- I say "details, schmetails" because it doesn't really matter. we could have an entire lecture on adding binary numbers. it would not improve your understanding of how a computer works.

## Slide 15: What goes into multi-bit adders; multi-bit wires?
in reality, a wire can only carry 1 bit.
but we're living in schematic-land.
if we want to, say, NOT a 32-bit value, we can draw it like:
32
32
this is shorthand for 32 parallel wires and 32 NOT gates.
Logisim calls these wires wire bundles and colors them black.
  it doesn't draw the slashes and numbers though…
orange wires happen when you have two things of different bit widths connected together.
  it's like a type error. you have to make sure the bit widths of the things on both ends are the same.

## Slide 16: A bundle of problems
more bits means bigger numbers and more computation at once!
  so why don’t we see 128-bit and 256-bit computers yet?
for a given word size, all the circuitry has to be built to support it.
to add two 64-bit numbers, you need:
  64 1-bit adders…
  128 wires going in…
  64 wires coming out…
wire bundles aren't real; real circuits have to deal with this problem!
  this is the problem of interconnect.
Notes: - this problem of interconnect is also where those blue X wires come in handy…
- in real circuits, you can save a LOT of space by reusing the same wire for multiple purposes
- that's called a bus, and buses rely on that blue X state to work properly.

## Slide 17: Flip side
remember how we do subtraction?
  x - y ==
  x + (-y) ==
  x + ~y + 1
we can NOT y with… what kind of gate?
how do we add 1 without any extra circuitry?
  we use a full adder for the LSB, and when we're subtracting, set the "carry in" to 1
  now we're doing x + ~y + 1!
+
~B0
A0
S0
+
~B1
A1
S1
1
Notes: - if you are seriously looking down here for the answer to “we can NOT y with what kind of gate?” I really don’t know what you expect to find.

## Slide 18: Integer Overflow

## Slide 19: Breaking the wall
we saw something weird when we looked at the number circles.
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
unsigned numbers:
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
signed numbers:
what is 14 + 5?
what is 6 + 3?
when we cross these lines ("go off the end of the number line")…
we get a number too big to be represented…
and it gets wrapped around.
this is overflow.
Notes: - if you go the other way (add a negative), it's still called overflow – the term “underflow” is used for like, tiny floating point numbers.

## Slide 20: How many bits?
if you add two 2-digit decimal numbers, what's the largest number you can get?
what about two 4-digit decimal numbers?
what about two 4-bit numbers?
what's the pattern of the number of digits?
  if you add two n-digit numbers in any base…
  the result will have at most n + 1 digits
that means if we add two 32-bit numbers…
  …we might get a 33-bit result that will not fit back into our 32-bit registers!
99
+99
198
9999
+9999
19998
1111
+1111
11110

## Slide 21: So you’ve got an overflow. Now what?

## Slide 22: Responding to Overflow
overflow is bad.
  it means we've passed the limits of what our computer can do.
so, once we've detected an overflow, we have three options:
  store
  ignore
  fall on the floor (crash)

## Slide 23: Facepalm
the worst and most common way to respond to overflow is…
IGNORE IT!!!
just keep going! pretend everything is fine!
but it's NOT fine
it's frustrating that this is the default in many popular languages… which is why we have addu/subu.
this is what MIPS addu/subu do.

## Slide 24: Open the door, fall on the floor
a better* response is to crash. (fall on the floor and cry.)
  in MIPS, the add and sub instructions crash… on signed overflow.
  (there are no MIPS instructions that crash on unsigned overflow.)
this generates a CPU Exception, which is kinda like a Java exception.
  these exceptions can be detected and handled.
Notes: * so, in high-reliability computing environments (think planes, spacecraft, medical life support), "crashing" is seen as a really bad thing.
- cause you don't want your plane dropping out of the air cause someone added two big numbers.
- however, there have been multiple lives lost due to integer overflow in software controlling these machines.
- see Therac-25, Toyotas' persistent "unintended acceleration" bugs…
- so like, maybe crashing and restarting would have saved those lives?
- it's not a black-and-white matter in all cases. but for non-life-critical programs, crashing might be the better response.
- it also points out these bugs to the developers much earlier/during development, instead of lingering as hidden issues for years.

## Slide 25: Maybe the bit bucket is a real place after all…
many other architectures do this, but MIPS does not.
instead of discarding the 33rd bit, we save it into a special register.
  this is the carry register. it's just 1 bit.
this gives the most flexibility:
  if a program wants to ignore it, it just… does.
  if a program wants to crash, it can check that register after the operation, and crash if the carry is 1 or 0 or whatever.
  but as a bonus, this lets us do arbitrary precision arithmetic.
Notes: - if it's so great, why doesn't MIPS have it?
- the carry register becomes an implicit operand/destination of several instructions, which gets confusing
- it also makes pipelining, superscalar, and out-of-order execution much more complicated.
- if that doesn't make sense to you, that's fine, it's 1541 stuff. but that's the main reason they ditched it in MIPS.

## Slide 26: Arbitrary-precision arithmetic (animated)
on an n-bit CPU, you are not limited to doing n-bit additions.
you can add any number of bits by doing multiple n-bit additions.
10101100
10101110
10101100
01011010
11101101
11100001
+00000100
00111110
if I want to add two 16-bit numbers on an 8-bit CPU...
I can do two 8-bit adds, starting with the LSB.
the carry bit from the first add is carried into the second add.
and I can keep chaining them together!
Notes: - arbitrarily many times! hence the name!
- this is common on embedded CPUs where the word size is small enough that many useful numbers are "too big" for one register…
- but it also pops up in things like cryptography where you need to deal with e.g. 2048-bit numbers, and no CPU can handle those in one register/instruction.

## Slide 27: Detecting overflow

## Slide 28: Detecting overflow: unsigned addition
the simplest case.
0111
+1100
0011
1 1 0 0
7
+12
3??
1
this is because the result is really 10011, but it was truncated to 4 bits, so it wrapped around.
in unsigned addition, if the MSB has a carry out of 1, an overflow happened.
but this rule doesn't work for signed addition…
Notes: - another way of thinking about it is that overflow occurs if you get a sum that is less than either of the addends.
- try to prove to yourself that you can't add two numbers and get a sum at least as big as one addend.
- think about the number circle. how "far around" can you get with a single addition?

## Slide 29: Detecting overflow: signed addition
this one's more subtle.
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
what are the two ways to cross the line?
1. add two positives, get a negative
2. add two negatives, get a positive
if we add numbers of opposite signs, it's impossible to cross the line.
is this possible?
no. the largest positive is 7; the furthest we could get is 6.
in signed addition, overflow occurs if we add two numbers of the same sign and get the opposite sign.
Notes: - another way to think of it is: adding numbers of opposite signs always gives you a number closer to 0.
- adding numbers of the same sign gets you further from 0, which is where the danger zone lies.
- it's impossible to flip signs twice with a single addition.

## Slide 30: Detecting overflow: signed subtraction
signed subtraction is really signed addition, so the same rule applies.
  you apply the rule after doing the negation, though.
0111
+1100
0011
7
+-4
3
7-4 = 7+(-4)
addends have opposite signs, so no overflow possible.
0111
+0100
1011
7
+4
-5
7-(-4) = 7+4
addends have same signs, and sum's sign differs: overflow!

## Slide 31: Detecting overflow: unsigned subtraction
1 1 1 0
remember: the two’s complement of a number behaves like its negative… and amazingly, this also works for unsigned numbers!
because of the number circle, there are two ways to get to 9 from 14.
1110
+1011
1001
14-5 = 14+(~5+1) = 14+11
14
+11
9
but wait – the MSB's carry out is 1. isn't that overflow?
for unsigned subtraction, overflow occurs when the MSB's carry out is 0, not 1.

## Slide 32: “Summing” it all up (ha ha ha ha ha oh god I’m sorry)
for all four operations, an overflow occurred if…
 | Addition | Subtraction
Unsigned |  | 
Signed |  | 
MSB’s carry-out is 1
MSB’s carry-out is 0
same sign inputs, opposite sign output (e.g. pos + pos = neg)
same as addition, but check after negating second input

## Slide 33: Detecting overflow in hardware

## Slide 34: Detecting unsigned overflow in hardware
MSB carry-out
how did we detect unsigned overflow?
  we can look at the MSB's carry-out.
when adding, if it's 1, it's an overflow.
when subtracting, if it's 0, it's an overflow.
  which interpretation is it? well, we'd have to make a decision…
  which we'll learn about shortly!
+
B0
A0
S0
+
B1
A1
S1
+
B2
A2
S2

## Slide 35: Detecting signed overflow in hardware
how did we detect signed overflow?
  same input signs; different output sign.
that feels truth-table-y.
SB
So
O
0
0
1
1
0
1
0
1
0
1
0
0
0
0
1
1
0
1
0
1
SA
0
0
0
0
1
1
1
1
0
0
1
0
when the input signs differ, we can't have an overflow, so those rows are all 0.
when the input signs match, overflow happens when the output sign differs.
and on the lab, you’ll turn this truth table into a circuit!
Notes: - oh, you're doing a lab about this, aren't you ;V