## Slide 1: Overflow
CS 0447
Jarrett Billingsley

## Slide 2: Class announcements
……. :(

## Slide 3: Integer Overflow

## Slide 4: Breaking the wall
we saw something weird when we looked at the number circles.
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
unsigned numbers:
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
signed numbers:
what is 14 + 5?
what is 6 + 3?
when we cross these lines ("go off the end of the number line")…
we get a number too big to be represented…
and it gets wrapped around.
this is overflow.
Notes: - if you go the other way (add a negative), it's still called overflow – the term “underflow” is used for like, tiny floating point numbers.

## Slide 5: How many bits?
if you add two 2-digit decimal numbers, what's the largest number you can get?
what about two 4-digit decimal numbers?
what about two 4-bit numbers?
what's the pattern of the number of digits?
  if you add two n-digit numbers in any base…
  the result will have at most n + 1 digits
that means if we add two 32-bit numbers…
  …we might get a 33-bit result that will not fit back into our 32-bit registers!
99
+99
198
9999
+9999
19998
1111
+1111
11110

## Slide 6: Detecting overflow: unsigned addition
the simplest case.
0111
+1100
0011
1 1 0 0
7
+12
3??
1
this is because the result is really 10011, but it was truncated to 4 bits, so it wrapped around.
in unsigned addition, if the MSB has a carry out of 1, an overflow happened.
but this rule doesn't work for signed addition…
Notes: - another way of thinking about it is that overflow occurs if you get a sum that is less than either of the addends.
- try to prove to yourself that you can't add two numbers and get a sum at least as big as one addend.
- think about the number circle. how "far around" can you get with a single addition?

## Slide 7: Detecting overflow: signed addition
this one's more subtle.
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
what are the two ways to cross the line?
1. add two positives, get a negative
2. add two negatives, get a positive
if we add numbers of opposite signs, it's impossible to cross the line.
is this possible?
no. the largest positive is 7; the furthest we could get is 6.
in signed addition, overflow occurs if we add two numbers of the same sign and get the opposite sign.
Notes: - another way to think of it is: adding numbers of opposite signs always gives you a number closer to 0.
- adding numbers of the same sign gets you further from 0, which is where the danger zone lies.
- it's impossible to flip signs twice with a single addition.

## Slide 8: Detecting overflow: signed subtraction
signed subtraction is really signed addition, so the same rule applies.
  you apply the rule after doing the negation, though.
0111
+1100
0011
7
+-4
3
7-4 = 7+(-4)
addends have opposite signs, so no overflow possible.
0111
+0100
1011
7
+4
-5
7-(-4) = 7+4
addends have same signs, and sum's sign differs: overflow!

## Slide 9: Detecting overflow: unsigned subtraction
1 1 1 0
remember: the two’s complement of a number behaves like its negative… and amazingly, this also works for unsigned numbers!
because of the number circle, there are two ways to get to 9 from 14.
1110
+1011
1001
14-5 = 14+(~5+1) = 14+11
14
+11
9
but wait – the MSB's carry out is 1. isn't that overflow?
for unsigned subtraction, overflow occurs when the MSB's carry out is 0, not 1.

## Slide 10: “Summing” it all up (ha ha ha ha ha oh god I’m sorry)
for all four operations, an overflow occurred if…
 | Addition | Subtraction
Unsigned |  | 
Signed |  | 
MSB’s carry-out is 1
MSB’s carry-out is 0
same sign inputs, opposite sign output (e.g. pos + pos = neg)
same as addition, but check after negating second input

## Slide 11: So you’ve got an overflow. Now what?

## Slide 12: Responding to Overflow
overflow is bad.
  it means we've passed the limits of what our computer can do.
so, once we've detected an overflow, we have three options:
  store
  ignore
  fall on the floor (crash)

## Slide 13: Facepalm
the worst and most common way to respond to overflow is…
IGNORE IT!!!
just keep going! pretend everything is fine!
but it's NOT fine
it's frustrating that this is the default in many popular languages… which is why we have addu/subu.
this is what MIPS addu/subu do.

## Slide 14: Open the door, fall on the floor
a better* response is to crash. (fall on the floor and cry.)
  in MIPS, the add and sub instructions crash… on signed overflow.
  (there are no MIPS instructions that crash on unsigned overflow.)
this generates a CPU Exception, which is kinda like a Java exception.
  these exceptions can be detected and handled.
Notes: * so, in high-reliability computing environments (think planes, spacecraft, medical life support), "crashing" is seen as a really bad thing.
- cause you don't want your plane dropping out of the air cause someone added two big numbers.
- however, there have been multiple lives lost due to integer overflow in software controlling these machines.
- see Therac-25, Toyotas' persistent "unintended acceleration" bugs…
- so like, maybe crashing and restarting would have saved those lives?
- it's not a black-and-white matter in all cases. but for non-life-critical programs, crashing might be the better response.
- it also points out these bugs to the developers much earlier/during development, instead of lingering as hidden issues for years.

## Slide 15: Maybe the bit bucket is a real place after all…
many other architectures do this, but MIPS does not.
instead of discarding the 33rd bit, we save it into a special register.
  this is the carry register. it's just 1 bit.
this gives the most flexibility:
  if a program wants to ignore it, it just… does.
  if a program wants to crash, it can check that register after the operation, and crash if the carry is 1 or 0 or whatever.
  but as a bonus, this lets us do arbitrary precision arithmetic.
Notes: - if it's so great, why doesn't MIPS have it?
- the carry register becomes an implicit operand/destination of several instructions, which gets confusing
- it also makes pipelining, superscalar, and out-of-order execution much more complicated.
- if that doesn't make sense to you, that's fine, it's 1541 stuff. but that's the main reason they ditched it in MIPS.

## Slide 16: Arbitrary-precision arithmetic (animated)
on an n-bit CPU, you are not limited to doing n-bit additions.
you can add any number of bits by doing multiple n-bit additions.
10101100
10101110
10101100
01011010
11101101
11100001
+00000100
00111110
if I want to add two 16-bit numbers on an 8-bit CPU...
I can do two 8-bit adds, starting with the LSB.
the carry bit from the first add is carried into the second add.
and I can keep chaining them together!
Notes: - arbitrarily many times! hence the name!
- this is common on embedded CPUs where the word size is small enough that many useful numbers are "too big" for one register…
- but it also pops up in things like cryptography where you need to deal with e.g. 2048-bit numbers, and no CPU can handle those in one register/instruction.