## Slide 1: Arithmetic and Decisions
CS 0447
Jarrett Billingsley

## Slide 2: Class announcements
:)

## Slide 3: Binary addition, in logic

## Slide 4: Solving problems with circuits
here's a surprising fact:
  all computation can be built from just the basic Boolean logic operations (AND, OR, and NOT).
  and since binary only has two values, anything expressed in binary can be computed using these logical operations.
our goal is to build an entire CPU.
  we'll hold off on the "reading instructions" and "taking steps" and "remembering stuff" until later.
  but we actually know enough to start building the ALU: the part of the CPU that, well, computes.

## Slide 5: Quick aside: truth tables with “multiple outputs”
we’ll be looking at several truth tables that look like this:
A | B | X | Y
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | 1 | 0
A | B | X
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
A | B | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
here A and B are inputs, and X and Y are outputs. if that looks weird, well:
it’s shorthand for two truth tables. we’re just saving space by not repeating the inputs.
=
Notes: - remember, functions can only have one output! often we want to have “multiple-bit outputs”, but we do that be implementing each bit of the output as its own function.

## Slide 6: Is a half-truth a lie?
let's come up with a truth table for adding two 1-bit numbers.
each column will hold 1 bit.
A
B
C
0
0
1
1
0
1
0
1
0
0
0
1
S
0
1
1
0
let's name the inputs A and B:
and let's name the outputs C and S, for Carry and Sum.
for the input values, we count up in binary…
now let's fill in the output values.
great! But this is wrong.
hey, this C column looks familiar… what about S?
Notes: - whenever making a truth table, ALWAYS count up in binary – it's so easy to miss cases if you jump around
- C and S form a 2-bit number
- C just looks like A & B
S looks like A xor B
well it’s not wrong, it’s just not the whole answer, because we almost always need to add more than two 1-bit numbers together!

## Slide 7: The full truth
what we just made was a half-adder.
it has a carry output but not a carry input.
  (which might be useful for the lowest bit)
    but might not be, as we'll see
to make a full adder, we need 3 input bits:
A
B
Co
0
0
1
1
0
1
0
1
0
0
0
1
S
0
1
1
0
0
0
1
1
0
1
0
1
Ci
0
0
0
0
1
1
1
1
0
1
1
0
1
0
1
1
00111 110
1011 0010
+0010 1111
1110 0001
A
B
Co
S
Ci
Notes: - Ci = Carry in, Co = Carry out

## Slide 8: The logic of it all
it looks a little messy, but it kinda makes sense if you think of it like this:
  it counts how many input bits are "1".
if we look at the outputs in isolation:
  S is 1 if we have an odd number of "1s"
  Co is 1 if we have 2 or 3 "1s”
actually coming up with collections of gates that output this truth table is kind of complicated, but I’m just gonna wave my hands and say…
  there's a full_adder.circ example circuit for you!
A
B
Co
0
0
1
1
0
1
0
1
0
0
0
1
S
0
1
1
0
0
0
1
1
0
1
0
1
Ci
0
0
0
0
1
1
1
1
0
1
1
0
1
0
1
1
Notes: - Again, Co and S are a 2-bit number
- it might not be obvious, but we can come up with a collection of gates that output each of these columns

## Slide 9: Sweeping that under the rug…
in programming, we use functions to be able to reuse code.
in schematics, we can group these 5 gates into a component.
here's the symbol for a one-bit full adder:
+
B
A
Ci
Co
S
inputs are like parameters…
and outputs are like return values.
now we don't have to care how it adds, just that it does.
unfortunately Logisim’s built-in adder flips this upside down but whatever.
Notes: - Logisim does this with a lot of components (puts the least significant bit up top instead of at the bottom) and I don't know why. most diagrams I've seen in texts put the LSB at the bottom.

## Slide 10: And that’s how we build circuits
the process of building any circuit goes something like this:
A | B | Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
1. make a truth table that expresses the computation we want.
2. turn the truth table into a Boolean expression.
3. turn that into logic gates.
A
B
Y
steps 1 and 3 are pretty straightforward, but step 2…
well, the lab will introduce you to a straightforward way to do that!
Notes: bubbles on the inputs of a gate are shorthand for a NOT gate on each bubbled input.
“turning a truth table into a boolean expression” can actually be a pretty complicated process! look up “karnaugh maps!”

## Slide 11: Adding (and subtracting) multi-bit numbers

## Slide 12: Where do the carries go?
when you add one place, you might get a carry out.
that bit becomes the carry in for the next higher place.
1 0 1 1 0 0 1 0
+0 0 1 0 1 1 1 1
Bit Bucket..?
Notes: - what is this called?
- how can we handle it?

## Slide 13: Ripple Carry
if we want to add two three-bit numbers, we'll need three one-bit adders!
we chain the carries from each place to the next higher place, like we do on paper.
we split the numbers up like so:
+
B0
A0
S0
+
B1
A1
S1
+
B2
A2
S2
A2 | A1 | A0
B2 | B1 | B0
S2 | S1 | S0
+
Logisim’s built-in multi-bit adders do this stuff for you.
Notes: - it's called ripple carry because the carry "ripples" from the LSB to the MSB one place at a time
- well, okay, Logisim's multi-bit adders are just using the + operator because they're written in Java but CONCEPTUALLY, OKAY?

## Slide 14: Propagation Delay
electrical signals can't move infinitely fast, and transistors can't turn on and off infinitely fast.
every gate and wire has propagation delay: the amount of time needed for a signal to “propagate” through it.
in a ripple carry adder, since each place must wait for the next smaller place to compute its “final answer” for its carry output…
  ripple carry is linear in the number of bits!
that means if you double the number of bits, you double the amount of time needed.
there are more efficient ways of adding…
  details, schmetails
+
B0
A0
S0
+
B1
A1
S1
+
B2
A2
S2
Notes: - carry lookahead adders are faster (constant time, O(1)!) but require O(n^2) space. there are several other kinds of adders too.
- I think there are also some diminishing returns there, so what you usually see is a weird hybrid approach:
- they do look-ahead carry on chunks of bits (fractions of the word size), and then ripple those carries to the next chunk of bits
- I say "details, schmetails" because it doesn't really matter. we could have an entire lecture on adding binary numbers. it would not improve your understanding of how a computer works.

## Slide 15: What goes into multi-bit adders; multi-bit wires?
in reality, a wire can only carry 1 bit.
but we're living in schematic-land.
if we want to, say, NOT a 32-bit value, we can draw it like:
32
32
this is shorthand for 32 parallel wires and 32 NOT gates.
Logisim calls these wires wire bundles and colors them black.
  it doesn't draw the slashes and numbers though…
orange wires happen when you have two things of different bit widths connected together.
  it's like a type error. you have to make sure the bit widths of the things on both ends are the same.

## Slide 16: A bundle of problems
more bits means bigger numbers and more computation at once!
  so why don’t we see 128-bit and 256-bit computers yet?
for a given word size, all the circuitry has to be built to support it.
to add two 64-bit numbers, you need:
  64 1-bit adders…
  128 wires going in…
  64 wires coming out…
wire bundles aren't real; real circuits have to deal with this problem!
  this is the problem of interconnect.
Notes: - this problem of interconnect is also where those blue X wires come in handy…
- in real circuits, you can save a LOT of space by reusing the same wire for multiple purposes
- that's called a bus, and buses rely on that blue X state to work properly.

## Slide 17: Flip side
remember how we do subtraction?
  x - y ==
  x + (-y) ==
  x + ~y + 1
we can NOT y with… what kind of gate?
how do we add 1 without any extra circuitry?
  we use a full adder for the LSB, and when we're subtracting, set the "carry in" to 1
  now we're doing x + ~y + 1!
+
~B0
A0
S0
+
~B1
A1
S1
1
Notes: - if you are seriously looking down here for the answer to “we can NOT y with what kind of gate?” I really don’t know what you expect to find.

## Slide 18: Detecting unsigned overflow in hardware
MSB carry-out
how did we detect unsigned overflow?
  we can look at the MSB's carry-out.
when adding, if it's 1, it's an overflow.
when subtracting, if it's 0, it's an overflow.
  which interpretation is it? well, we'd have to make a decision…
  which we'll learn about shortly!
+
B0
A0
S0
+
B1
A1
S1
+
B2
A2
S2

## Slide 19: Detecting signed overflow in hardware
how did we detect signed overflow?
  same input signs; different output sign.
that feels truth-table-y.
SB
So
O
0
0
1
1
0
1
0
1
0
1
0
0
0
0
1
1
0
1
0
1
SA
0
0
0
0
1
1
1
1
0
0
1
0
when the input signs differ, we can't have an overflow, so those rows are all 0.
when the input signs match, overflow happens when the output sign differs.
and on the lab, you’ll turn this truth table into a circuit!
Notes: - oh, you're doing a lab about this, aren't you ;V

## Slide 20: Hardware that makes decisions

## Slide 21: How you're used to doing it
how do we make decisions in programming?
  with if-elses, conditional loops, switches…
if(mode == 1)
return A & B;
else
return A + B;
if mode == 1, is the else clause run?
No.
when you make a decision in software, only one code path is run; the others never happen.

## Slide 22: How hardware does it
instead of making the decision first and then doing one thing…
hardware does all possible things, then decides which to use.
and = A & B;
sum = A + B;
if(mode == 1)
return and;
else
return sum;
when you make a decision in hardware, you do all possible things, then pick only the thing you need, and ignore the rest.
this seems wasteful, but: these two paths can be done at the same time!
hardware is really good at doing things in parallel, so we may as well.
Notes: - counterintuitively, it can actually be more complex to "do one thing" than to "do all things."
- but, that can make your circuits more energy-efficient, so a lot of recent CPU designs include this sort of thing.
- look up "clock gating;" basically, you turn off the parts of the CPU that you aren't using at any given time.

## Slide 23: Multiplexers
a multiplexer (mux) outputs one of its inputs based on a select.
Y
A
B
S
This is the select input.
Y
A
B
S=0
A
Y
B
S=1
the unselected input is ignored!
Notes: - muxes are universal too! you can build any logic gate – and therefore an entire computer – out of muxes

## Slide 24: Implementing this if-else
now we have enough information to do this:
if(mode == 1)
return A & B;
else
return A + B;
mode
result
the select signal is basically the condition.
+
A
B
if
else
we send the input values to all possible branches.
Notes: …and this would be one of those “multi-bit AND gates”. (which is really multiple AND gates in parallel.)

## Slide 25: Big muxes
a mux can have any (power-of-2) number of inputs
here's one with 4 inputs!
to choose among 4 values… how big does the select signal have to be now?
  2 bits.
Y
A
B
S
C
D
2
00
01
10
11
this is a bit like a hardware switch-case.

## Slide 26: Warning: demultipliexers considered pointless
a demultiplexer (demux) is the opposite of a multiplexer, but...
In
S
In
S=0
0
In
S=1
0
with very few exceptions, you won't need these.
95% of the times I've seen people using them, they're pointless.
but hold that thought for later.
Notes: - when we get to register files and instruction decoding, these will become useful!