## Slide 1: The Control
CS 0447
Jarrett Billingsley

## Slide 2: Class announcements
:V

## Slide 3: The Control

## Slide 4: Controlling the datapath
last time, we put together this thing, which we call the datapath:
Register File
imm field
ALU
MemWE
ALUBSrc
ALUOp
rd
RegWE
RegDataSrc
rs
rt
Data Memory
Data
Address
this can do the work of instructions, but it can’t read them.
how can we use this to implement add? sub? addi? lw? sw?
we need something to automatically set all those blue control signals.
Notes: - frustratingly if you look up what “datapath” means, it’s more like “the ALU”, but colloquially everyone (even the book which gives that definition!) uses it to mean “the entire part of the CPU responsible for manipulating data, including the register file and memory”
- again, computer scientists are bad at naming things (or being consistent with the meanings of words)
- add and sub would turn on RegWE; set RegDataSrc to use the ALU output; set ALUSrc to use the register; and set ALUOp appropriately.
- addi would do almost the same, except set ALUSrc to use the immediate.
- lw would set ALUSrc to immediate; ALUOp to add; set RegDataSrc to memory; and turn on RegWE.
sw would be similar to lw, but turn on MemWE instead of RegWE.
it's like a weird, awkward calculator at this point. you can use it to do calculations, but you have to do it all manually.

## Slide 5: Feeling nervous
Data Memory
the control is what automatically sets the control signals to the right values to make each instruction happen.
it's like the CPU's brain and nervous system.
Control
c'mon you lazy bums
Register File
ALU
awwwww we don't wannaaaa
it does this by reading the instructions.
sub v0, t0, t1
Register file, read t0 and t1, and write to v0. ALU, do subtraction. Interconnect, route the data from the two registers into the ALU and from the ALU into the register file. Data memory, you get to take a break.
yissssss
👀

## Slide 6: Instruction Execution

## Slide 7: The real phases of instruction execution
Fetch (IF or F)
  use PC to get the next instruction from memory
Decode (ID or D)
  look at the fetched instruction and set control signals
Execute (EX or X)
  wait for data to flow through the ALU
Memory Access (MEM or M)
  if it's a load or store, do that
Write-back (WB or W)
  if there's a destination register, write the result to it
F
D
X
M
W
often we can do multiple phases "at the same time."
Notes: - every instruction will have a fetch and decode phase.
- almost all instructions have an execute phase (except for a no-op).
- only loads and stores have a memory phase.
- only instructions with destination registers have a write-back phase.

## Slide 8: Which parts do what
Instruction Memory
PC FSM
Control
Register File
ALU
Data Memory
F
D
W
X
M

## Slide 9: Single-cycle machine control
we'll be talking about a single-cycle machine and building one for the project
this means each instruction takes one clock cycle to execute
add t0, t1, t2
sb t0, 4(s0)
do F, D, X…
W: store sum in t0
M: store value in memory
do F, D, X…
each instruction ends on the rising edge of the clock.
(that's when the registers/memory store the computed values.)

## Slide 10: That's fine for Harvard architectures…
but what about von Neumann architectures, with 1 memory?
Memory
PC FSM
Control
Register File
ALU
so, the control and the rest of the CPU have to take turns.
the memory is now used for both the F and M phases.
which means each instruction takes multiple steps…
Notes: - remember, 1 memory = von Neumann, 2 memories = Harvard

## Slide 11: Multi-cycle machine control
the simplest multi-cycle machine takes two cycles per instruction:
sb t0, 4(s0)
use memory for M: store value
use memory for F...
D, X…
save the fetched instruction into the control!
now the control has to remember which state it's in as well as what the fetched instruction was.
so a multi-cycle control unit is an FSM.
Notes: - the register in the control that saves the fetched instruction is a microarchitectural register
- it's hidden from view, but needed to implement the ISA
- it's often called IR for "instruction register", which makes sense
- of course, we need another microarchitectural register to keep track of what state the control is in
- here we only have two states: "Fetch" and "Everything Else"
- but we can take this concept much, much further…

## Slide 12: Single-cycle Control

## Slide 13: The control hardware
in a single-cycle machine, the control's job is straightforward:
Instruction Memory
address goes in…
…instruction comes out.
MemWE
ALUSrc
ALUOp
rd
RegWE
RegDataSrc
rs
rt
immediate
Jump
Control
instruction goes in…
…control signals come out.
PC FSM
Branch

## Slide 14: The steps
there are three main phases of decoding:
  split the encoded bitfield into its constituent values.
  from the opcode, determine which instruction we're looking at.
  map that instruction to a unique combination of control signals.
all of this should happen inside the control unit!
  when you get to the project, do not sprinkle bits of control all over your CPU! it gets really, really confusing!

## Slide 15: Pull 'n' peel
the first step is to split the encoded instruction up
but which instruction format is it? actually, it doesn't matter.
do everything at once, but use only what you need.
31 | 26 | 25 | 21 | 20 | 16 | 15 | 0
opcode |  | rs |  | rt |  | immediate | 
31 | 26 | 25 | 21 | 20 | 16 | 15 | 11 | 10 | 6 | 5 | 0
opcode |  | rs |  | rt |  | rd |  | shamt |  | funct | 
31 | 26 | 25 |  | 0
opcode |  | target |  | 
31-26
opcode
25-21
rs
20-16
rt
15-11
rd
10-6
shamt
5-0
funct
15-0
immediate
25-0
target
32
instruction
R
I
J
see splitter_bitfields.circ and decoding.circ.

## Slide 16: No, really, it's fine, don't worry about it
let's suppose the encoded instruction was addi s0, s0, -1.
op
rs
rt
rd
shamt
funct
imm
target
32
0x2210FFFF
addi s0,s0,-1
0x08
0x10
0x10
0x1F
0x1F
0x3F
0xFFFF
0x210FFFF
31 | 26 | 25 | 21 | 20 | 16 | 15 | 0
opcode |  | rs |  | rt |  | immediate | 
put it through the splitter and…
…out come a bunch of values.
the opcode identifies this as addi, which is an I-type instruction.
therefore, rs, rt, and immediate will be used….
…and the R- and J-type fields are bogus and will be ignored.
Notes: - how does the CPU know it's an I-type instruction?
- well that's like asking: how does a paper hole puncher "know" how far apart to put the holes?
- it… doesn't. we just designed it to do that. it punches the holes that far apart because the punchers are that far apart.
- the control is as dumb as the rest of the CPU. it's mechanical. it sees opcode 8, it will use those fields.

## Slide 17: From opcode to control signals
the control is a boolean function that takes the instruction opcode as its input and outputs the control signals.
in other words, it's a big fat truth table!
opcode | Jump | RegDataSrc | RegWE | ALUOp | …
000000 | 0 | 00 | 0 | 000 | …
000001 | 0 | 01 | 1 | 110 | …
000010 | 0 | 00 | 1 | 010 | …
000011 | 1 | 00 | 0 | 011 | …
000100 | 1 | 11 | 1 | 000 | …
000101 | 0 | 10 | 1 | 010 | …
… | … | … | … | … | …
I really would not recommend making a control unit like this.
you will go insane.
it's time-consuming, confusing, hard to debug, and hard to change.
I just made up these numbers. Please don't try to use them.

## Slide 18: First: identifying which instruction we're looking at
a decoder takes a number and turns on one output; the rest are 0.
so, if we feed it an opcode, it will tell us which instruction it is.
opcode
<r-type>
<misc>
j
jal
beq
bne
blez
bgtz
addi
addiu
slti
sltiu
at any time, exactly one of these will be on (1).
note: these are not the control signals! we use these as inputs to logic in order to come up with the control signals.
for that, it's good to focus on one control signal at a time.
e.g. if the current instruction is a jal, the jal wire will be 1.
Notes: - to be clear: these signals are 1 if the opcode says "yes it's this instruction" and 0 otherwise.

## Slide 19: The logic of a control signal
let's focus on a really simple control signal: MemWE.
  this is the write enable for the data memory.
so, which 3 MIPS instructions write to (store into) memory?
  sw, sh, and sb
if you were writing it as code, it might be something like…
  if(opcode == sw || opcode == sb || opcode == sh)
  MemWE = true
  else
  MemWE = false
or even more tersely:
  MemWE = opcode == sw || opcode == sb || opcode == sh
that seems really easy to turn into a circuit!

## Slide 20: <the sound a seal makes>
those instruction signals are 1 when the opcode is that instruction.
so, we just… OR them together in this case.
sw
sh
sb
MemWE
this says, "if we are executing a sw, or a sh, or a sb instruction, we are writing to memory, so turn on its write enable."
other single-bit control signals can be done similarly.
consider RegWE, RegDataSrc, ALUSrc…

## Slide 21: Multi-bit control signals
what about multi-bit control signals, like ALUOp?
  that might be as much as 4 bits to select a dozen operations.
one approach is to use enormous MUXes to select constants.
opcode
ALUOp
ALUOp for opcode 0
ALUOp for opcode 1
ALUOp for opcode 2
ALUOp for opcode 3
ALUOp for opcode 4
ALUOp for opcode 5
ALUOp for opcode 6
ALUOp for opcode 7
ALUOp for opcode 8
ALUOp for opcode 9
ALUOp for opcode A
ALUOp for opcode B
ALUOp for opcode C
it… works, but it's hard to follow.
it's hard to tell which constant is used for which instruction.
it's also hard to add new instructions.
so let’s learn about one more component that will help us.
Notes: - remember, MUXes are universal… you could make your whole CPU out of em. (please do not.)

## Slide 22: Priority Encoders
a priority encoder is kind of the opposite of a decoder.
you give it several 1-bit inputs, and it tells you which one is 1.
Pri
1
0
0
0
0
Pri
0
1
0
0
1
Pri
0
1
0
0
2
Pri
0
1
0
0
3
Pri
0
0
0
0
X
if none of the inputs is 1, then it gives you X…
to avoid this, you must put a constant 1 as the first input.
Notes: - putting the 1 as the first input is like saying "else, the output is 0".

## Slide 23: Multi-bit control signals
let's say we have these instructions, and these ALU operations.
for each input, ask: which instructions need this ALU operation?
add
addi
sub
subi
and
or
0: &
1: |
2: +
3: -
ALUOp
Pri
1
sub
subi
add
addi
or
ALUOp 0 is the default, so and is handled.
which instruction(s) need OR (1)?
what about + (2)?
what about - (3)?
think of it like an upside-down if-else-if…
instructions to support
ALUOp values
Notes: the numbers of the ALU operations are decided by the MUX in the ALU.
you could read this as saying "if the instruction is sub or subi, aluop = 3. else if it's add or addi, aluop = 2. else if it's or, aluop = 1. else, aluop = 0."

## Slide 24: The overall “shape” of control
the only input is the current instruction, which gets split up.
the outputs are some instruction fields and the control signals.
opcode
rd
rs
rt
…
rd
rs
rt
MemWE
ALUOp
…
the opcode gets decoded to produce the instruction signals.
hlt
li
put
add
sub
lw
…
the instruction signals are used to come up with the control signals.
Pri
1
ALUOp
sub
and
not
li
add
sub
RegWE
not
…

## Slide 25: Summary
in a single-cycle machine, the control is a big combinational circuit.
it takes as its input the machine code instruction to execute…
  and it outputs every control signal for the whole CPU.
and that’s it! it’s big, and has lots of parts, but each part is simple.
  that simplicity is going to be a problem when we try to use this in a real-world CPU design though…